## Slide 1: J/Psi in the Coil
Chris and Leslie
4th June 2015

## Slide 2: Data in Target with Chris’ cuts
Cuts used:
Two muons only.
No other track from vertex
-1.0 < (P- - P+) / (P- + P+) <0.0
(Before correction)
P- , P+ each > 1 GeV/c
Pparent > 5 GeV/c

## Slide 3: Old look at coil data
We do not have a good treatment of extrapolating through coil and of adding dE/dx.
I have added dEdx by hand, but angle still not right.
I had divided the coil data into two halves:
-24.0 to -42.0 Downstream
-70.0 to -42.0 Upstream
Used same cuts as for Target.

## Slide 4: Quick look at coil data
Downstream
Upstream
The Downstream showed a small enhancement as in the target.
The Upstream does not.
But now I find that the coil is 23cm thick -24  -50 approximately

## Slide 5: New look at coil data
I now divided the old coil data into two more reasonable halves:
-50.0 to -24.0 Should be the correct coil.
-70.0 to -50.0 Whatever is upstream.
Now more reasonable: Signal in coil, but NOT outside.

## Slide 6: Fit to coil data: -50.0  -24.0
Now more reasonable: Signal in coil, but NOT outside.
Using the exact same limits as for the Target:
13.8±5.7 events in signal
Background 19.2
Significance: 3.2s
Background subtracted

## Slide 7: Coil mass corrections
The coil effective density must be reduced for gaps in its construction and for the cooling water
Geometry correction:
Width: 785 x 4 + 94 x 2 + 200 =3528mm Area = 3528 x 4000 = 14.11 m2
Remove: 2 x 94 x 4000 + 300 x p2 + 200 x (4000-600) = (0.752+0.283+0.680)m2 = 1.72m2
Geometry correction: (14.11-1.72)/14.11 = 0.878
Cooling water correction:
{(55x55- p x 11.52 )x 2.7gm.cm-3 + p x 11.52 x 1 gm.cm-3}/{55 x 55 x 2.7gm.cm-3} = 0.914
Overall correction: 0.878 x 0.914 = 0.802
The corrections below
are based on numbers
in this figure describing
the NOMAD coil.

## Slide 8: Approximate efficiency and rates
Looked at target data as a funcion of Z
It is weighted.
Fit as a function of z between +80 and +390 cm
Sweight=0.274+0.780x 10-4 x Z
Small dependence.
Extrapolate to -37cm  0.271
Sum of generated weights: 27.1
Per bin: 27.1/40
Efficiency per bin: 0.271/ (27.1/40) = 0.4
[Efficiency for whole target was 0.402
The Reason it’s not much higher in target is the
Missing chambers at times.]
I see 18.2 events in target
Thickness of coil vs target= (2.7 x 23)/(0.1x410) = 62.1/41=1.5
So we expect in coil: 1.5 x18.2 x 0.802 = 22 events
Two slides back We see ~13.8 ±5.7 ~2 s low

## Slide 9: All events: -50.0 to +405.0cm Target +Coil
Nice signal!

## Slide 10: Fit to coil + Target data: z :-50.0  + 405.0 cm
Signal: 35.1±9.3
Background: 50.8
Significance: 4.9s

## Slide 11: Conclusion
The coil signal is there!
The earlier division is downstream/upstream of coil was wrong!
We should see a few more events in the coil.
Adding the coil + target data results in a good signal.